## Slide 14
ASSUMPTION
PLANE SECTION NORMAL TO THE AXIS REMAIN PLANE AFTER BENDING.
THE MAXIMUM STRAIN IN CONCRETE AT THE OUTERMOST COMPRESSION FIBRE IS TAKEN AS 0.0035.
THE TENSILE STRENGTH OF THE CONCRETE IS IGNORED.
THE STRESS BLOCK MAY BE ASSUMED AS RECTANGLE, TRAPEZOID, PARABOLA OR ANY OTHER SHAPE WHICH RESULTS IN PREDICTION OF STRENGTH IN SUBSTANTIAL AGREEMENT WITH THE RESULTS OF THE TEST.

## Slide 15
ASSUMPTIONS (CONTINUED…)
5. THE STRESSES IN THE REINFORCEMENT ARE DERIVED FROM REPRESENTATIVE STRESS – STRAIN CURVE FOR THE TYPE OF STEEL USED.
FOR DESIGN PURPOSE, THE PARTIAL SAFETY FACTOR
= 1.15 shall be applied.
6. THE MAXIMUM STRAIN IN THE TENSION REINFORCEMENT IN THE SECTION AT THE FAILURE SHALL NOT BE LESS THAN

## Slide 16
Specially for limit state of collapse : compression
The maximum compression strain in concrete in axial compression is taken as 0.002.
The maximum compressive strain at the highly compressed extreme fibre in concrete subjected to axial compression and bending and when there is no tension on the section shall be 0.0035 minus 0.75 times the strain at the least compression fibre.